Vertical Orbit Excursion FFAGs and Other Things

---
Horizontal SC magnet problem
- Getting vertical B field requires same-direction current windings (nearby)
- By proportional to x/(a^2+x^2)
a

---
Horizontal SC magnet variation
- Getting horizontal B field requires opposite current windings and is easier
- Bx proportional to a/(a^2+x^2)
a

---
Vertical SC magnet
- But now the field is in the wrong direction!
- That's OK, rotate the magnet
- The dipole field is there
- But what sort of focussing does this magnet give?

---
“Scaling” VFFAG magnet
- Dipole field should increase moving up the magnet, so set By=exp(ky) on axis (x=0)
- Subtracting dipole component leaves the field of a skew quad:
Exponential is good because moving upwards just scales the field and all gradients
Thus closed orbits at different momenta are exactly the same shape, just translated upwards
VFFAG = Vertical orbit excursion FFAG

---
Scaling VFFAG Field Formula

---
FODO Scaling VFFAG Machine
Simulation

---
Scaling VFFAG Tracking

---
VFFAG Acceleration

---
Windings for Magnet

---
Scaling (V)FFAG disease
- This ring has unlimited energy range (until the maximum magnet field is reached)
- Constant tunes
- Space charge is probably a smaller term than intrinsic nonlinearities, need to check
- Unfortunately it is about 10x larger than ISIS instead of the desired 2x
  - Defocussing is locked to reverse bending, as in scaling FFAGs

---
Search for “lopsided” lattices
- 10000 particles were tracked for 1km
- Survival rate plotted on axes of lengths of “F” and “D” type magnets
- This reveals both the lattice stability region and resonance stop-bands

---
Lattices can't be very lopsided
- Unfortunately in all cases the region of dynamic stability sticks very close to the F=D diagonal line
  - So pure exponential VFFAGs will always be big, with much reverse bending
- Another reason for choosing the non-scaling machine initially was to ensure msot magnets contribute to the bend
  - Thus, non-scaling VFFAG? Interesting!

---
Convert EMMA to VFFAG Study

---
Normal Conducting Magnets?
:)

---
Fixed tune non-scaling FFAGs
- In principle if you have at least three free magnet gradients, you can simultaneously satify the equations
- Sum of dipole = momentum * constant
- d(X tune)/dp = d(Y tune)/dp = 0
- Thus, Grahame's pumplet lattice
  - 1-2-3 configuration also possible

---
Two Magnet Families Only

---
FFAG Master Table

---
FFAGs Master Table

---
3D “Necktie” Diagram

---
3D “Necktie” Diagram

---
Three Magnet Families?

---
References
- Stephen Brooks
  - HB2010 “Vertical Orbit Excursion FFAGs”
  - IPAC'11 “Three-Lens Lattices for Extending the Energy Range of Non-scaling FFAGs”
  - http://stephenbrooks.org/ral/report/ (EMMA)
- “Theory of the ring cyclotron”, A.P. Fateev, J. Nucl. Energy, Part C Plasma Phys. 4 p.64 (1962). http://iopscience.iop.org/0368-3281/4/1/110