## Slide 1: CBETA: a 4-pass superconducting ERL with combined permanent magnet return arc

## Slide 2: Layout & Parameters
Main linac is a 1.3GHz SCRF module with six 5-cell cavities
±36MeV
6MeV
6MeV
42-150MeV
42,78,114,150MeV
Source
Injector cryomodule
Main linac cryomodule
Beam stop
Diagnostic line
Splitter A
Splitter B
Arc A
Arc B
Transition B
Transition A
Straight

## Slide 3: Bunch Pattern (one option)
Time structure as seen by the main linac

## Slide 4: What can an ERL do?
Applications: thin targets, electron coolers, Compton backscattering, light sources, electron-ion colliders (LHeC/FCC-eh)
 | Advantages | Disadvantages
Compared to linac | Energy recovery: circulating beam power can be much higher than RF power input | Can’t use stopping targets! Disrupted beam must survive 1 turn (or a few turns)
Compared to ring | Equivalent to ring with cooling system that cools in one turn! (small emittance) Can disrupt beam more than in a ring where beam has to survive millions of turns | Source current must equal circulating current; Current in linac is circulating current multiplied by 2 or more (important for higher order modes)

## Slide 5: CBETA Energy Saving Technologies
Permanent magnets
Superconducting RF
Energy recovery (above 6MeV)
Recirculation: 4x beamline reuse, 4x energy
Funded by NYSERDA
  (NY State Energy R&D Authority)
  $25M grant
  Cornell already had the injector & cryomodule

## Slide 6: Project Timeline
Construction
Beam operation

## Slide 7: Fixed-Field Return Loop Optics
Beams with 4x rigidity range transmitted through same overall radius of curvature in arcs
Adiabatically merged to zero curvature, separation in straights
Beam cell tune decreases as a function of energy

## Slide 9: Permanent Magnet Design
Halbach design made of NdFeB material
This is a combined dipole+quad
Being measured on rotating coil at BNL
3D printed multipole corrector pack inside
Windowframe corrector coil outside
Temperature stabilised by water (orange hoses)

## Slide 10: Fixed-Field Return Arc

## Slide 11: Main Linac Cryomodule

## Slide 12: Possible Halo after Injector
3×10-4 relative intensity
~100x beam core area
About 3% of total charge
Probably from photocathode
(April 17, 2019)
Selectively-activated photocathode has been used before at Cornell to suppress this sort of thing
Collimators in the injector are possible but harder due to high beam powers

## Slide 14: Commissioning results: orbit correction in fixed-field loop
The very first beam through the fixed-field loop on May 7, 2019
Corrected beam
(June 12, 2019)

## Slide 15: Cell Tunes in Beam Energy Scan
Fixed-field arcs
Fixed-field straight
(June 12, 2019)

## Slide 16: Higher Current Test / Radiation
Using ~3pC bunches
Halo just went through
Current limited by uninteresting things:
Wrong gun photocathode
Fast EPS not installed (10uA limit)
Gun resistor needs changing
External radiation monitors (70uA limit)
No “physics” current limit seen
Extrapolating internal FFA losses gives 70uA*(10000/600) = 1.17mA limit
1mA should be fine
Probably 1-10mA CSR limit

## Slide 17: Dispersion, R56 correction
Beam entering the dump line is steady, free of RF energy jitter (July 13, 2019)

## Slide 18: Energy Recovery Efficiency
Transmission improved to 99.6 ± 0.1%
Average current increased to 8 μA
Beam loading for each cavity shown on the right
-•- ER mode -•- Non-ER mode
Load Deviation (W)
Load Deviation (W)
Current (μA)
Current (μA)
K. Deitrick - kd324@cornell.edu
NAPAC 2019 - Status of the CBETA Prototype

## Slide 19: Next: 4-turn operation
Beam on ~mid-October
Other splitter lines have been installed during summer shutdown

## Slide 20: Future: CBETA Facility?
ERL experiment
ERL experiment
RLA experiment
Vertical double chicane
User experiments platform
Single-turn mode with reduced CSR and increased current 40+mA, 55MeV
High energy mode with 3 turns in fixed-field arc, 1-10mA, 200MeV

## Slide 21: Bypass Design (Kirsten Deitrick)
Single-turn mode with reduced CSR and increased current 40+mA, 55MeV
High energy mode with 3 turns in fixed-field arc, 1-10mA, 200MeV
One possible route is for the bypass to follow above the FFA arcs

## Slide 22: BACKUP

## Slide 23
Energy Recovery
Increased beam current to calculate transmission using RF load due to beam on MLC cavities
  Total RF load = RF load for cavity field + RF load due to beam (rough approximation)
  As beam current changes, the load deviation is due to the changing RF load due to beam
First, demonstrate measurable load deviation in the MLC up to 1 μA without recirculated beam (non-ER mode)
In perfect energy recovery mode, two conditions are satisfied:
  There is no load deviation at any beam current
  The linear fit of load deviation as a function of beam current is zero
To measure energy recovery transmission, determine linear fit of load deviation as a function of current for each MLC cavity
  The closer each linear fit slope is to zero, the better the energy recovery
K. Deitrick - kd324@cornell.edu
NAPAC 2019 - Status of the CBETA Prototype

## Slide 24
Energy Recovery
To demonstrate load deviation in MLC cavity, the each cavity was set up near typical field – but the last three cavities decelerated the beam, sending it directly into the beam stop
MLC labeled layout shown below, typical beam loading plots for accelerating (cavities 4-6) and decelerating (cavities 1-3) shown to the right
Load Deviation (W)
Load Deviation (W)
Current (μA)
Current (μA)
K. Deitrick - kd324@cornell.edu
NAPAC 2019 - Status of the CBETA Prototype

## Slide 25
Energy Recovery
First transmission calculation of 87.0 ± 0.6% on June 24, 2019
Beam loading for each cavity shown on the right
ER mode Non-ER mode
Load Deviation (W)
Load Deviation (W)
Current (μA)
Current (μA)
Current (μA)
K. Deitrick - kd324@cornell.edu
NAPAC 2019 - Status of the CBETA Prototype

## Slide 26
Energy Recovery
Transmission improved to 99.3 ± 0.2% (two days later)
Beam loading for each cavity shown on the right
ER mode Non-ER mode
Load Deviation (W)
Load Deviation (W)
Current (μA)
Current (μA)
Current (μA)
K. Deitrick - kd324@cornell.edu
NAPAC 2019 - Status of the CBETA Prototype

## Slide 27
Better Energy Recovery, Higher Current
Transmission improved to 99.6 ± 0.1%
Average current increased to 8 μA
Beam loading for each cavity shown on the right
ER mode Non-ER mode
Load Deviation (W)
Load Deviation (W)
Current (μA)
Current (μA)
Current (μA)
K. Deitrick - kd324@cornell.edu
NAPAC 2019 - Status of the CBETA Prototype

## Slide 28
ERL Frontier: Tennant Plot
eRHIC cooler
K. Deitrick - kd324@cornell.edu
NAPAC 2019 - Status of the CBETA Prototype